## Slide 1
Contamination
Concentration of contaminant C0 = 1000 mg/L
Concentration of contaminant
0 mg/L
Contamination
Concentration of contaminant C0 = 1000 mg/L
Concentration of contaminant
Cx=3ft, t mg/L
Flow due to advection
Contaminant transport due to diffusion
Cutoff wall made with a low-permeability material that has an ability to sorb contaminant
Initial state
After ‘t’ years
Contaminant transport due to diffusion
Ct at t= 5 years (mg/L) |  | 
Method | With sorption (Kd =3 cm3/g) | Without sorption
Advective-diffusion (exact method, Ogata and Banks Solution) | 0 | 69.6
Advective-diffusion (approximate method, first term of Ogata and Banks Solution) | 0 | 31.4
Diffusion only | 0 | 103.5
To estimate contaminant breakthrough concentration at x=3 ft (example with initial concentration of contaminant = 1000 mg/L):
Flow due to advection
After ‘t’ years
EL=500 ft
EL=501 ft
3 ft
EL=501 ft
EL=500 ft