## Slide 1
Cyclic liquefaction
Occurs on both level or sloping ground
Triggered by:
  an earthquake
  heavy machinery that vibrates during operation
  anything that creates a strong rapid cyclic loading event
Examples: Niigata earthquake in 1964
Slow (drained) loading can trigger static liquefaction.
The liquefaction event, once triggered, is very rapid (undrained).
Fast (undrained) loading triggers cyclic liquefaction.
The liquefaction event, once triggered, is very rapid (undrained).
Static liquefaction
Occurs on sloping ground, e.g., dams, tailings storage facilities (TSFs)
Triggered by:
    the placement of static load
    raise in the phreatic surface
    basal extrusion (i.e., lateral horizontal displacement of the foundation
Examples: Mount Polley TSF failure in 2014 Cadia TSF failure in 2018, Brumadinho TSF failure in 2019